## Slide 1
A fast, physics-informed neural surrogate
for CHO bioreactor dynamics
Forecasting a full cell-culture run from its first few days
Neve Callaway Lab meeting · 2026

## Slide 2
The problem, and the goal
The reference model. COSMIC dynamic flux-balance analysis: a system of ODEs that turns fluxes and feed conditions into the daily trajectory of a cell culture. Accurate, but slow to solve.
The goal. Replace the solver with a small neural network that forecasts the whole run, cell density, metabolites, antibody titer, from the early days plus the operating conditions.
Why it matters. Thousands of times faster, and differentiable, so it plugs into design and optimization.
en primeur
Judging a wine before it is bottled, tasting the young vintage to forecast the finished product.
This project does the same for a bioreactor: predict the finished run from its first few days.

## Slide 3
Three models, in order of how much physics they embed
1
Pure NN
Predicts next-day concentrations directly. No ODE at all. The control that shows the ODE is not what makes it accurate.
2
Hybrid neural-ODE
The network predicts per-cell fluxes; a fixed ODE step integrates them. Mass balance by construction. ODE in the forward pass.
3
Physics-informed (PINN)
Predicts concentrations, with the ODE only as a soft training penalty. Solver-free at inference, so it keeps the speedup.

## Slide 4
You were right #1: look at the loss curves
We had no validation split. We added one, and it changed the story twice:
The small-data model was under-training, not over-fitting.
It corrected an earlier result we had overstated.
Best-epoch numbers alone were misleading, the curve is what showed it.
Demanding the curves is what surfaced this.
Chart: MSE loss vs epoch (val stays flat = no over-training)
| 25 | 50 | 75 | 100 | 125 | 150
train | 0.00056 | 0.0005 | 0.0005 | 0.00046 | 0.00046 | 0.00048
validation | 0.00043 | 0.00028 | 0.00029 | 0.00028 | 0.00027 | 0.00034

## Slide 5
Accuracy: on R², the metric you asked for
R² = how much of the true variation the model explains (1 = exact, 0 = no better than the mean). Unitless, and stricter than shape alone.
ρ = does the prediction move up and down with the truth (shape only). n/a on a flat signal: nothing to correlate.
Zero-negative synthetic data, no clamp.
feature | R² | ρ | 
Cell density | 0.98 | 0.91 | 
Cell size | 0.98 | 1.00 | 
Titer | 0.95 | 0.97 | scored
Glucose | 0.99 | 0.97 | 
Glycine | 0.95 | 0.53 | 
Glutamine | n/a | 0.62 | 
Asparagine | n/a | 0.63 | dynamic,
Serine | n/a | 0.49 | tracked
5 of 8 score R² 0.95–0.99 (small model: 1 conv layer, hidden 32, chosen for xAI). Amino acids read n/a on the flat-window rule.

## Slide 6
How the model does: predicted vs true
Points on the diagonal = perfect. Every variable hugs the line, including the three amino acids (bottom row), which now spread along the diagonal instead of collapsing to a flat blob.

## Slide 7
A forecast in action: titer
Black = the true run. Red dashed = the NN's forecast. The model sees only days 0–6 (left of the line), then predicts the peak and decline of days 6–12 on its own. R² 0.97.

## Slide 8
A data-generation bug we found and fixed
Symptom. Three amino acids were flat in our synthetic data, but the real measurements show them changing a lot.
Cause. The starting pool was tied to a 210×-inflated feed, pinning each amino acid at its feed level.
Fix (no clamp). Separate the starting pool from the feed, size the feed minimally, and raise the glucose feed. Result: real dynamics and zero negative values, surfaced, never clamped.
Chart: Glutamine (normalized) vs day
| 0 | 2 | 4 | 6 | 8 | 10 | 12
before fix (flat) | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5 | 0.5
after fix (dynamic) | 0.35 | 0.95 | 0.86 | 0.62 | 0.5 | 0.42 | 0.3

## Slide 9
Inference: NN vs the mechanistic model
~15 min → 0.0013 ms
COSMIC-dFBA takes ~15 minutes per reactor (Sarat: 3.7 GHz CPU, no parallelization, 1-day resolution). The NN predicts the same run in 0.0013 ms, hundreds of millions of times faster.
Honest caveat (Sarat). Any empirical model beats a mechanistic flux-balance simulation, so this is expected. COSMIC-dFBA's niche is mechanistic insight; the speed enables real-time use, it is not the contribution.
A separate comparison: our fast synthetic generator (a simplified ODE, what we train on), not COSMIC-dFBA:
method | ms/reactor | vs scipy
numerical ODE (scipy, CPU) | 25.25 | 1×
closed-form ODE (GPU) | 0.0005 | 47,000×
pure NN (GPU, small) | 0.0005 | 47,000×
A100, n = 20,000, small net (1 conv, hidden 32). The NN ties the exact closed-form ODE; this is our simplified generator, COSMIC-dFBA (~15 min) is off this chart entirely.

## Slide 10
Why it matters
Media design
A model that predicts state change better than random has learned what drives it. Read those importances out (sensitivity, attention, SHAP) and you get which conditions and media components matter. This does not depend on speed.
Real-time monitoring
A fast, interpretable surrogate enables Process Analytical Technology and Real-Time Release Testing, prediction and explanation during a run, not offline.
Precedent: Patel & Patel (2026) use SHAP on Raman spectra to find the drivers of glucose and acetate, toward PAT/RTRT.

## Slide 11
Physics in training, none at inference (the PINN)
Exactly the physics-informed design you suggested, not the ODE in the forward pass.
window
1D CNN
attention
conc head
flux head
used at inference ✓
training only (ODE penalty)
Result. A small physics weight (λ ≈ 0.1) steadies the cell-density forecast, correlation 0.79 → 0.89, with the solver absent at inference.
The ODE lives only in the loss; at inference we use the concentration head alone.

## Slide 12
Scope and next steps
Data and scope
Trained on synthetic data, a physics analog of the real reactors. Real data is not used for training or magnitudes.
Normalized after combining all data, so scaling is invertible and concentrations stay interpretable. Cross-sample variance preserved.
Success = profiles match the simulator. Window-level holdout, 1–2 windows per reactor. Cell density first (R² 0.99).
Real data and next steps
Real data only as a loose shape/trend check, never magnitude. Conditions largely differ (shared: perfusion rate, eta switch, operating factors, O₂).
Lazy training: add data for each new condition as it is encountered and retrain (~4 min). The hard part is detecting out-of-distribution inputs, knowing when to add.
Hybrid ODE-in-forward inference timing; continuous-time PINN.

## Slide 13
Where we landed
Two of your points, the loss curves and the benchmark, changed our conclusions for the better.
A physics-informed surrogate is built: accuracy is honest (R² 0.97–1.00 on 5 of 8 variables).
We found and fixed a data-generation bug, no clamp, zero negatives.
Everything is documented and reproducible for the next person.
en Primeur