## Slide 1
A fast neural surrogate of a
Mechanistic CHO bioreactor model
Forecasting final conditions from the first few days
Neve Callaway Lewis Lab meeting · 2026

## Slide 2
We Can Train a Small Surrogate NN for COSMIC-dFBA
Reference model: COSMIC dynamic flux balance analysis (dFBA) solves a system of ODEs to predict daily cell culture dynamics from metabolic rates (feed, washout, uptake, and secretion).
Accurate, but computationally slow
Goal: Use a small neural network trained on COSMIC-dFBA simulations to rapidly forecast the remaining culture trajectory from early observations and operating conditions.
So, why EN PRIMEUR?
Faster inference
Differentiable
Reveals influential inputs (feature importance)
Guides media design and optimization
Confidence limits
EN PRIMEUR
French term for the practice of tasting a young wine from the barrel and predicting the final vintage before purchase.
Similarly, this framework learns to forecast a bioreactor’s trajectory and final conditions from early-run data.

## Slide 3
Model architecture
The small model: one 1D conv layer, 32 hidden nodes. Every node drawn as a dot.
input
9 (x 6 days)
1D CNN → Attention pool
32 (x 6 days)
+ DoE
35
hidden
32
next day
8
Arrows = flow between layers, not full connectivity. Gold dots = the 3 DoE (operating-condition) inputs.
Each prediction feeds back in to forecast the rest of the run. The hybrid and PINN variants add a flux head (32 → 8), feeding an ODE step or a physics penalty.
Weighted summary of all
6 previous days
32
Concentration head

## Slide 4
Performance Metrics
R² = how much of the true variation the model explains (1 = exact, 0 = no better than the mean). Unitless, and stricter than shape alone.
ρ = does the prediction move up and down with the truth (shape only). n/a on a flat signal: nothing to correlate.
feature | R² | ρ
Cell density | 0.98 | 0.91
Cell size | 0.98 | 1.00
Titer | 0.95 | 0.97
Glucose | 0.99 | 0.97
Glycine | 0.95 | 0.53
Glutamine | n/a | 0.62
Asparagine | n/a | 0.63
Serine | n/a | 0.49
5 of 8 variables score R² 0.95–0.99. 3 amino acids are too flat to score (n/a) but the model still tracks them.

## Slide 5
The Model’s Predicted v. True
Points falling on the diagonal = perfect. Every variable hugs the line, including the three amino acids (bottom row), which now spread along the diagonal instead of collapsing to a flat blob.

## Slide 6
Titer Predictions
Black = the ground truth synthetically generated run. Red dashed = the NN's forecast. The model sees only days 0–6 (left of the line), then predicts the peak and decline of days 6–12 on its own.

## Slide 7
Cell Density Predictions
Black = the ground truth synthetically generated run. Red dashed = the NN's forecast. The model sees only days 0–6 (left of the line), then predicts the peak and decline of days 6–12 on its own.

## Slide 8
Cell Size Predictions
Black = the ground truth synthetically generated run. Red dashed = the NN's forecast. The model sees only days 0–6 (left of the line), then predicts the peak and decline of days 6–12 on its own.

## Slide 9
Glucose Predictions
Black = the ground truth synthetically generated run. Red dashed = the NN's forecast. The model sees only days 0–6 (left of the line), then predicts the peak and decline of days 6–12 on its own.

## Slide 10
Inference: NN vs the mechanistic model
~15 min → 0.0013 ms
COSMIC-dFBA takes ~15 minutes per reactor. The NN predicts the same run in 0.0013 ms, hundreds of millions of times faster.
Perspective (Sarat). Any empirical model will outperform a mechanistic flux-balance simulation in speed, so this result is expected.
A separate comparison: our fast synthetic generator (a simplified ODE, what we train on), not COSMIC-dFBA:
method | ms/reactor | vs scipy
numerical ODE (scipy, CPU) | 25.25 | 1×
closed-form ODE (GPU) | 0.0005 | 47,000×
pure NN (GPU, small) | 0.0005 | 47,000×
Setup: 1 GPU, 20,000 reactors, small net (1 conv, hidden 32). On this chart the NN ties the exact closed-form ODE, but this is our simplified generator (the fast ODE we train on).

## Slide 11
Why it matters
It's a differentiable, statistical model, not a mechanistic solver, so it can do things the solver can't:
1 Fast done
Milliseconds vs ~15 min per run. Cheap enough to run thousands of times, scan conditions, retrain on demand.
2 Differentiable inherent
You can take gradients, so you can optimize for a target (e.g. maximize titer) and see how sensitive the output is to each input. A solver can't.
3 Feature importances next step
Read out which conditions and media components drive the outcome, i.e. which knobs matter, toward media design.
4 Confidence limits next step
The model can report how confident it is: prediction intervals, not just a single number.

## Slide 12
Three potential models, in order of how much physics they embed
1
Pure NN
Predicts next-day concentrations directly, no ODE or physics inside the model. It's the control: it shows the ODE isn't what makes the prediction accurate.
2
Hybrid neural-ODE
The network predicts per-cell fluxes, and a fixed ODE step integrates them into the next-day concentrations. Mass balance is guaranteed. The ODE runs in the forward pass.
3
Physics-informed (PINN)
Predicts concentrations directly. During training, the ODE is added to the loss as a soft penalty that nudges the model toward the physics; at inference it's gone entirely, so it runs as a plain, fast NN pass.

## Slide 13
Scope and next steps
Data and scope
Trained on synthetic data, a physics analog of the real reactors. Real data is not used for training or magnitudes.
Normalized after combining all data, so scaling is invertible and concentrations stay interpretable. Cross-sample variance preserved.
Success = profiles match the simulator. Window-level holdout for validation, 1–2 windows per reactor.
Real data and next steps
Real data only as a loose shape/trend check, never magnitude. Conditions largely differ (shared: perfusion rate, eta switch, operating factors, O₂).
Lazy training: add data for each new condition as it is encountered and retrain (~4 min).
Hybrid ODE-in-forward inference timing and continuous-time PINN could be explored
Find more?